## Slide 1: 22.3MB1 Electromagnetism Dr Andy Harvey e-mail a.r.harvey@hw.ac.uk lecture notes are at: http://www.cee.hw.ac.uk/~arharvey/22.3MB1electromagnetism.zip
Revision of Electrostatics (week 1)
Vector Calculus (week 2-4)
Maxwell’s equations in integral and differential form (week 5)
Electromagnetic wave behaviour from Maxwell’s equations (week 6-7.5)
  Heuristic description of the generation of EM waves
  Mathematical derivation of EM waves in free space
  Relationship between E and H
  EM waves in materials
  Boundary conditions for EM waves
Fourier description of EM waves (week 7.5-8)
Reflection and transmission of EM waves from materials (week 9-10)
Notes: The high cost of commercial and military thermal imaging systems is due to the optical components which are made with the high cost materials and require complex manufacturing.
The conventional approach achieves high performance imaging by employing a complex sequences of lenses or increasing lens complexity and this add to the cost, size and weight of the imaging systems.
While the cost of producing lenses is relatively constant over the time, the improvements in electronic technology make the cost of digital signal processing exponentially decreasing (Moor’s law).

## Slide 2: Maxwell’s equations in differential form
Varying E and H fields are coupled
NB Equations brought from elsewhere, or to be carried on to next page, highlighted in this colour
NB Important results highlighted in this colour

## Slide 3: Fields at large distances from charges and current sources
For a straight conductor the magnetic field is given by Ampere’s law
I
H
dH/dt produces E
dE/dt term produces H
etc.
How do the mixed-up E and H fields spread out from a modulated current ?
  eg current loop, antenna etc
At large distances or high frequencies H(t,d) lags I(t,d=0) due to propagation time
  Transmission of field is not instantaneous
  Actually H(t,d) is due to I(t-d/c,d=0)
Modulation of I(t) produces a dH/dt term

## Slide 4: A moving point charge:
A static charge produces radial field lines
Constant velocity, acceleration and finite propagation speed distorts the field line
Propagation of kinks in E field lines which produces kinks of and
Changes in E couple into H & v.v
  Fields due to are short range
  Fields due to propagate
Accelerating charges produce travelling waves consisting coupled modulations of E and H

## Slide 5: Depiction of fields propagating from an accelerating point charge
Fields propagate at c=1/xm/sec
E in plane of page
H in and out of page

## Slide 6: Examples of EM waves due to accelerating charges
Bremstrahlung - “breaking radiation”
Synchrotron emission
Magnetron
Modulated current in antennas
  sinusoidal v.important
Blackbody radiation

## Slide 7: 2.2 Electromagnetic waves in lossless media - Maxwell’s equations
SI Units
J Amp/ metre2
D Coulomb/metre2
H Amps/metre
B Tesla Weber/metre2 Volt-Second/metre2
E Volt/metre
 Farad/metre
 Henry/metre
 Siemen/metre
Maxwell
Equation of continuity
Constitutive relations

## Slide 8: 2.6 Wave equations in free space
In free space
  =0 J=0
  Hence:
  Taking curl of both sides of latter equation:

## Slide 9: Wave equations in free space cont.
It has been shown (last week) that for any vector A
where is the Laplacian operator
Thus:
There are no free charges in free space so .E==0 and we get
A three dimensional wave equation

## Slide 10
Both E and H obey second order partial differential wave equations:
Wave equations in free space cont.
What does this mean
  dimensional analysis ?
   has units of velocity-2
  Why is this a wave with velocity 1/ ?

## Slide 11: The wave equation
v
Substitute back into the above EM 3D wave equation
This is a travelling wave if
In free space
Why is this a travelling wave ?
A 1D travelling wave has a solution of the form:
Constant for a
travelling wave

## Slide 12: Wave equations in free space cont.
Substitute this 1D expression into 3D ‘wave equation’ (Ey=Ez=0):
Sinusoidal variation in E or H is a solution ton the wave equation

## Slide 13: Summary of wave equations in free space cont.
Maxwells equations lead to the three-dimensional wave equation to describe the propagation of E and H fields
Plane sinusoidal waves are a solution to the 3D wave equation
Wave equations are linear
  All temporal field variations can be decomposed into Fourier components
    wave equation describes the propagation of an arbitrary disturbance
  All waves can be written as a superposition of plane waves (again by Fourier analysis)
    wave equation describes the propagation of arbitrary wave fronts in free space.

## Slide 14: Summary of the generation of travelling waves
We see that travelling waves are set up when
  accelerating charges
  but there is also a field due to Coulomb’s law:
  For a spherical travelling wave, the power carried by the travelling wave obeys an inverse square law (conservation of energy)
    P E2 1/r2
      to be discussed later in the course
    E/r
  Coulomb field decays more rapidly than travelling field
  At large distances the field due to the travelling wave is much larger than the ‘near-field’

## Slide 15: Heuristic summary of the generation of travelling waves
E due to stationary charge (1/r2)
due to charge
constant velocity (1/ r2)
kinks due to charge
acceleration (1/r)
due to E (1/r)

## Slide 16: 2.8 Uniform plane waves - transverse relation of E and H
Consider a uniform plane wave, propagating in the z direction. E is independent of x and y
In a source free region, .D= =0 (Gauss’ law) :
E is independent of x and y, so
So for a plane wave, E has no component in the direction of propagation. Similarly for H.
Plane waves have only transverse E and H components.

## Slide 17: Orthogonal relationship between E and H:
For a plane z-directed wave there are no variations along x and y:
Equating terms:
and likewise for :
Spatial rate of change of H is proportionate to the temporal rate of change of the orthogonal component of E & v.v. at the same point in space

## Slide 18: Orthogonal and phase relationship between E and H:
Consider a linearly polarised wave that has a transverse component in (say) the y direction only:
Similarly
H and E are in phase and orthogonal

## Slide 19
The ratio of the magnetic to electric fields strengths is: which has units of impedance
Note:
and the impedance of free space is:

## Slide 20: Orientation of E and H
For any medium the intrinsic impedance is denoted by  and taking the scalar product so E and H are mutually orthogonal
Taking the cross product of E and H we get the direction of wave propagation

## Slide 21: A ‘horizontally’ polarised wave
Hy
Ex
Sinusoidal variation of E and H
E and H in phase and orthogonal

## Slide 22: A block of space containing an EM plane wave
Every point in 3D space is characterised by
  Ex, Ey, Ez
  Which determine
    Hx, Hy, Hz
    and vice versa
  3 degrees of freedom

Hy
Ex

## Slide 23: An example application of Maxwell’s equations: The Magnetron

## Slide 24: The magnetron
Poynting vector S
Displacement current, D
Current, J
Lorentz force F=qvB
Locate features:

## Slide 25: Power flow of EM radiation
Intuitively power flows in the direction of propagation
  in the direction of EH
What are the units of EH?
  H2=.(Amps/metre)2 =Watts/metre2 (cf I2R)
  E2/=(Volts/metre)2 / =Watts/metre2 (cf I2R)
Is this really power flow ?

## Slide 26: Power flow of EM radiation cont.
Energy stored in the EM field in the thin box is:

Hy
Ex
dx
Area A
Power transmitted through the box is dU/dt=dU/(dx/c)....

## Slide 27: Power flow of EM radiation cont.
This is the instantaneous power flow
  Half is contained in the electric component
  Half is contained in the magnetic component
E varies sinusoidal, so the average value of S is obtained as:
S is the Poynting vector and indicates the direction and magnitude of power flow in the EM field.

## Slide 28: Example problem
The door of a microwave oven is left open
  estimate the peak E and H strengths in the aperture of the door.
  Which plane contains both E and H vectors ?
  What parameters and equations are required?
    Power-750 W
    Area of aperture - 0.3 x 0.2 m
    impedance of free space - 377 
    Poynting vector:

## Slide 29: Solution

## Slide 30
Suppose the microwave source is omnidirectional and displaced horizontally at a displacement of 100 km. Neglecting the effect of the ground:
Is the E-field
  a) vertical
  b) horizontal
  c) radially outwards
  d) radially inwards
  e) either a) or b)
Does the Poynting vector point
  a) radially outwards
  b) radially inwards
  c) at right angles to a vector from the observer to the source
To calculate the strength of the E-field should one
  a) Apply the inverse square law to the power generated
  b) Apply a 1/r law to the E field generated
  c) Employ Coulomb’s 1/r2 law

## Slide 31: Field due to a 1 kW omnidirectional generator (cont.)

## Slide 32: 4.1 Polarisation
In treating Maxwells equations we referred to components of E and H along the x,y,z directions
  Ex, Ey, Ez and Hx, Hy, Hz
For a plane (single frequency) EM wave
  Ez=Hz =0
  the wave can be fully described by either its E components or its H components
  It is more usual to describe a wave in terms of its E components
    It is more easily measured
  A wave that has the E-vector in the x-direction only is said to be polarised in the x direction
    similarly for the y direction

## Slide 33: Polarisation cont..
Normally the cardinal axes are Earth-referenced
  Refer to horizontally or vertically polarised
  The field oscillates in one plane only and is referred to as linear polarisation
    Generated by simple antennas, some lasers, reflections off dielectrics
  Polarised receivers must be correctly aligned to receive a specific polarisation
A horizontal polarised wave generated by a horizontal dipole and incident upon horizontal and vertical dipoles

## Slide 34: Horizontal and vertical linear polarisation

## Slide 35: Linear polarisation
If both Ex and Ey are present and in phase then components add linearly to form a wave that is linearly polarised signal at angle
Horizontal
polarisation
Vertical
polarisation
Co-phased vertical+horizontal
=slant Polarisation


## Slide 36: Slant linear polarisation
Slant polarised waves generated by co-phased horizontal and vertical dipoles and incident upon horizontal and vertical dipoles

## Slide 37: Circular polarisation
RHC polarisation
LHC polarisation
NB viewed as approaching wave

## Slide 38: Circular polarisation
LHC & RHC polarised waves generated by quadrature -phased horizontal and vertical dipoles and incident upon horizontal and vertical dipoles
LHC
RHC

## Slide 39: Elliptical polarisation - an example

## Slide 40: Constitutive relations
permittivity of free space =8.85 x 10-12 F/m
permeability of free space o=4x10-7 H/m
Normally r(dielectric constant) andr
  vary with material
  are frequency dependant
    For non-magnetic materials r ~1 and for Fe is ~200,000
    ris normally a few ~2.25 for glass at optical frequencies
  are normally simple scalars (i.e. for isotropic materials) so that D and E are parallel and B and H are parallel
    For ferroelectrics and ferromagnetics r and r depend on the relative orientation of the material and the applied field:
At
microwave
frequencies:

## Slide 41: Constitutive relations cont...
What is the relationship between  and refractive index for non magnetic materials ?
  v=c/n is the speed of light in a material of refractive index n
  For glass and many plastics at optical frequencies
    n~1.5
    r~2.25
Impedance is lower within a dielectric
What happens at the boundary between materials of different n,r,r ?

## Slide 42: Why are boundary conditions important ?
When a free-space electromagnetic wave is incident upon a medium secondary waves are
  transmitted wave
  reflected wave
The transmitted wave is due to the E and H fields at the boundary as seen from the incident side
The reflected wave is due to the E and H fields at the boundary as seen from the transmitted side
To calculate the transmitted and reflected fields we need to know the fields at the boundary
  These are determined by the boundary conditions

## Slide 43: Boundary Conditions cont.
At a boundary between two media, r,r are different on either side.
An abrupt change in these values changes the characteristic impedance experienced by propagating waves
Discontinuities results in partial reflection and transmission of EM waves
The characteristics of the reflected and transmitted waves can be determined from a solution of Maxwells equations along the boundary
2,22
1,11

## Slide 44: 2.3 Boundary conditions
The tangential component of E is continuous at a surface of discontinuity
  E1t,= E2t
Except for a perfect conductor, the tangential component of H is continuous at a surface of discontinuity
  H1t,= H2t
E1t, H1t
2,22
1,11
E2t, H2t
2,22
1,11
D1n, B1n
D2n, B2n
The normal component of D is continuous at the surface of a discontinuity if there is no surface charge density. If there is surface charge density D is discontinuous by an amount equal to the surface charge density.
  D1n,= D2n+s
The normal component of B is continuous at the surface of discontinuity
  B1n,= B2n

## Slide 45: Proof of boundary conditions - continuity of Et
Integral form of Faraday’s law:
0
0
0
0
0
That is, the tangential component of E is continuous
2,22
1,11

## Slide 46: Proof of boundary conditions - continuity of Ht
Ampere’s law
That is, the tangential component of H is continuous
0
0
0
0
0
2,22
1,11

## Slide 47
The integral form of Gauss’ law for electrostatics is:
Proof of boundary conditions - Dn
applied to the box gives
hence
The change in the normal component of D at a boundary is equal to the surface charge density
2,22
1,11

## Slide 48: Proof of boundary conditions - Dn cont.
For an insulator with no static electric charge s=0
For a conductor all charge flows to the surface and for an infinite, plane surface is uniformly distributed with area charge density s
In a good conductor,  is large, D=E0 hence if medium 2 is a good conductor

## Slide 49
Proof of boundary conditions - Bn
Proof follows same argument as for Dn on page 47,
The integral form of Gauss’ law for magnetostatics is
  there are no isolated magnetic poles
The normal component of B at a boundary is always continuous at a boundary

## Slide 50: 2.6 Conditions at a perfect conductor
In a perfect conductor  is infinite
Practical conductors (copper, aluminium silver) have very large  and field solutions assuming infinite  can be accurate enough for many applications
  Finite values of conductivity are important in calculating Ohmic loss
For a conducting medium
  J=E
    infinite  infinite J
    More practically,  is very large, E is very small (0) and J is finite

## Slide 51
It will be shown that at high frequencies J is confined to a surface layer with a depth known as the skin depth
With increasing frequency and conductivity the skin depth, x becomes thinner
2.6 Conditions at a perfect conductor
Lower frequencies, smaller 
Higher frequencies, larger 
x
x
Current sheet
It becomes more appropriate to consider the current density in terms of current per unit with:

## Slide 52
Ampere’s law:
That is, the tangential component of H is discontinuous by an amount equal to the surface current density
Jszx
0
0
0
0
2,22
1,11
Conditions at a perfect conductor cont. (page 47 revisited)

## Slide 53: Conditions at a perfect conductor cont. (page 47 revisited) cont.
From Maxwell’s equations:
  If in a conductor E=0 then dE/dT=0
  Since
  Hx2=0 (it has no time-varying component and also cannot be established from zero)
The current per unit width, Js, along the surface of a perfect conductor is equal to the magnetic field just outside the surface:
H and J and the surface normal, n, are mutually perpendicular:

## Slide 54: Summary of Boundary conditions

At a boundary between non-conducting media
At a metallic boundary (large )
At a perfectly conducting boundary

## Slide 55: 2.6.1 The wave equation for a conducting medium
Revisit page 8 derivation of the wave equation with J0
As on page 8:

## Slide 56: 2.6.1 The wave equation for a conducting medium cont.
In the absence of sources hence:
This is the wave equation for a decaying wave
  to be continued...